## Slide 1
BloodHound RCEV
Remotely Controlled Electric Vehicle
Noah Holloway & Micah Spencer | ISU RCET Capstone | Spring 2026
[IMAGE: Bloodhound ATV photo]

## Slide 2
INTRODUCTION
What is the Bloodhound?
A repurposed Kawasaki 450 ATV frame converted into a remotely controlled electric vehicle
Designed to operate in hazardous environments — without putting a human operator at risk
Powered by a 52V LiFePO4 battery with dual 48V brushless hub motors (front-wheel drive)
Steering is handled by a DOCYKE power steering servo mounted directly to the steering column
Built and tested in 8 weeks as an ISU RCET capstone project
[IMAGE: Bloodhound frame/hardware photo from lab]
[IMAGE: Bloodhound frame/hardware photo]

## Slide 3
HARDWARE
Hardware Overview
Vehicle Platform
Kawasaki 450 frame, suspension & wheels
2× 48V brushless hub motors
2× 2-mode brushless speed controllers
DOCYKE S350 power steering servo (12–18 Nm torque)
Electronics
52V LiFePO4 battery with BMS (30Ah)
DC/DC converter: 52V → 24V for servo & boards
3 custom PCBs: URC, Master Main Board, Slave Dev Board
All PIC16F1788 / PIC16LF1789 microcontrollers
[IMAGE: Photo of all 3 PCBs side by side, or mounted on vehicle panel]

## Slide 4
SYSTEM ARCHITECTURE
Three-Board Architecture
URC
Universal Remote Controller
PIC16LF1789 (44-pin)
MASTER
Master Main Board
PIC16F1788 (28-pin)
SLAVE
Slave Dev Board
PIC16F1788 (28-pin)
UART 115,200 bps Wireless
I2C 100 kHz Wired
Outputs from Slave Board:
PWM → Motor Controllers
PWM → DOCYKE Servo (steering)
Brake & Direction signals
[IMAGE: Block diagram from report, or photo of wired boards together]

## Slide 5
COMMUNICATION
How Data Flows: URC → Master → Slave
Step 1 — Operator moves joystick on the URC
  Joystick position captured as 0–255 analog value; packaged into a 6-byte UART packet
Step 2 — Packet travels over wireless UART at 115,200 bps to the Master board
  Packet includes: sync byte (0x24), robot address, command type, and 3 data bytes
Step 3 — Master decodes the packet and every 96ms sends I2C data to the Slave
  I2C transaction: START → address (0x20) → 4 data bytes → ACK each → STOP
Step 4 — Slave receives I2C bytes, interprets joystick values, and updates outputs
  After all 4 bytes arrive, I2C_RX_COMPLETE flag triggers motor and servo updates

## Slide 6
COMMUNICATION DEEP DIVE
I2C Data Packets Explained
Byte 1
JOY1_UD
Drive Throttle
(Joystick 1 Up/Down)
Byte 2
JOY1_LR
Unused
(future use)
Byte 3
JOY2_UD
Brake trigger
(Joystick 2 Up/Down)
Byte 4
JOY2_LR
Steering
(Joystick 2 Left/Right)
How the values are interpreted:
Each joystick axis arrives as a byte: 0 = full left/back, 128 = center, 255 = full right/forward
Slave compares values to thresholds (Upper: 160, Lower: 80) to determine direction
Values outside the deadband are mapped proportionally to motor duty cycle or servo position

## Slide 7
FIRMWARE DEEP DIVE
Slave Board: Data → Physical Action
Timer 2 ISR fires every 0.1ms — the heartbeat of all output signals
  Software PWM: counts ticks to generate precise pulse widths for servo and motor controllers
Servo (DOCYKE): 50Hz signal, 1.2ms = full right, 1.5ms = center, 1.9ms = full left
Motor controllers: PWM duty sets speed; separate direction and brake pins control mode
Each I2C packet triggers UPDATE_DRIVE_STATUS → threshold check → set motor duty + servo
No I2C for ~260ms? → I2C_COM_TIMEOUT fires → brakes engage, all outputs go to stop
[IMAGE: Oscilloscope screenshot of PWM signal on RA4 (servo) or RA0 (motor)]

## Slide 8
SAFETY
Built-In Safety: Two Watchdogs
UART Watchdog (Master)
Timer 2 counts time between valid UART packets
No packet in ~0.5 seconds → CONNECT_TIMEOUT
Triggers a controller disconnect routine
Protects against loss of wireless signal
I2C Watchdog (Slave)
Timer 1 counts time between I2C data packets
No packet in ~260ms → I2C_COM_TIMEOUT
Immediately engages brakes and stops all motors
Prevents runaway if Master board fails
[IMAGE: Oscilloscope capture showing brake signal asserting after cable pull]

## Slide 9
RESULTS
What We Achieved
Reliable wireless UART communication between URC and Master board
Full I2C communication chain: Master → Slave, 4-byte packets at 96ms intervals
Joystick-controlled forward and reverse drive on both hub motors
Proportional steering via DOCYKE servo responding to joystick input
Electronic braking — I2C timeout automatically engages brakes within 260ms
System recovers automatically when connection is restored (no reboot needed)
RTK GPS module started — partially functional (requires further tuning)
[IMAGE: Bloodhound being driven in the lab — action shot if available]

## Slide 10
CONCLUSION
Future Expansion & Takeaways
Planned Additions
Front camera + backup camera (auto-switch on reverse)
Remotely-controlled headlights via button on URC
IMU / accelerometer for orientation data
LiDAR for obstacle detection
Chemical sensors: CO and CO2 detection
RTK GPS for precise positioning
Key Takeaways
Modular architecture — adding new slave boards is simple by design
Hardware bugs (missing MOSFETs, wrong T2CON) can look like firmware issues
Version control matters — working code was lost to an external tool and had to be restored
A structured troubleshooting procedure saved significant time
Thank you — Questions?